## Slide 1
  New adjustment block/oven support: Independent setting of neck cooling shield for more stability.
  Ecoven module for lamps cooling: The Super Cobra is replaced by a fan dedicated to each module.
  Heating modules: Only 8 IR lamps, more efficient lamps, ceramic wall and top reflector.
  Ceramic oven top reflector, adjustable in height to fit all preform lengths.
  Wiring: Pre-wired cabinet added to supply power to the fans.
  New automation and process: Updated main electrical cabinet (power supply, new functionalities and readjustment of all process sheets).
BENEFITS
20% to 45% less electrical consumption.
Fewer lamps for 11% less installed power.
Sharper heating: Sharp zoning on preform surface and optimized under-neck stretching.
Easier to maintain: Heating module can be serviced on the bench while the machine runs with a spare module.
Ceramics are self-cleaning via pyrolysis effect.
DESCRIPTION
ECOVEN
Ref. 1021 - 20% to 45% less electrical consumption
50k €*
Budget price:
TBD
Payback estimation:
18 to 22 MenDays
Installation time:
TBD
Machine downtime:
*according to blower size and scope, installation not included.
Can be combined with:
All Universal except Predis C3 & C5.
Machine application:
TBD
Sustainability
KEY FIGURES