## Slide 1
Dust and Particles (PET, plastic, wood, carton, …) which may accumulate inside the preforms are removed out by a filtered air flow, blown through injection nozzles.
PET dust removed up to 100% (mini 97%).
Contributes to filled Product Quality, specifically in Blowing-Filling-Capping COMBI configuration.
BENEFITS
  Complete module for preforms internal walls dedusting with:
    a rotary carrousel of cleaning air injection nozzles located between the oven infeed wheel and the preform infeed rail.
    blown air filtration 0.01 µm and exhaust flow manifold with filters.
      transfer wheel and related transmission to convey preforms up to oven loading.
      oven housing extension to integrate the module.
DESCRITPION
PREFORM DE-DUSTING MODULE
Ref. 1050
160 k€ *
Budget price:
Product Quality
Payback estimation:
18 men*days
Installation time:
6-8 working days
Machine downtime:
* MM size, installation not included.
Can be combined with:
Universal
All size of blower
Matrix with #2011
Blower S2 with #506
Machine application:
Ionised Air System on Preform rail - #2082
Rocking Hopper cover - #1016
Deflector inside Preform hopper #2067
PRODUCT QUALITY
KEY FIGURES