## Slide 1: Secure the right glue quantity on each label
VALUE AND BENEFITS
DESCRIPTION
New Glue Roller – pack “a”
Value: Efficiency, Maintenance, Obsolescence
Equipment: Labellers F15 Evo, Rollquattro, Rollquattro Evo, Matrix, Sidel Super Combi, EvoDECO
Catalogue code: AA27a
Secure production by replacing obsolete components (chromium rollers not manufactured any more) with latest technology glue roller
Prevent glue splashing and filaments guaranteed by “niches” shape;
Secure the proper quantity of glue applied on the label;
Better control of quantity of glue applied: if more glue is needed it is enough to increase the niches’ volume and the label pads’ area;
Reduce maintenance costs and machine downtime:
  recommended roller replacement jump from 9000 h with actual version to 36000h with new version
  Scrapper Life time doubled
  Reduced cost of replacement parts ( on average -15%)
Being the existing glue roller technology obsolete, Sidel provides an new assembly to deliver the right glue quantity on label:
  Auto-adjustable glue bar with an integrated scraper system
  New concept of glue transfer with controlled temperature
  Niches created with a laser cutting
The pack contains the necessary unassembled parts for the installation of the new glue roller.